Step 1 : As with all methods, the first step is preprocessing part. When the preprocessing part
is over, the lanes must be detected.

Step 1 : As with all methods, the first step is preprocessing phase. When the preprocessing phase is over, it must be find out, between which vertically pixels are the lanes stand.

Step 2 : Secondly, the positions of the lanes should be found. In order to find the positions of
the lanes, the Standard Hough Transformation is used. But the Standard Hough Transformation
should not utilize the entire frame; rather, the frame is cropped. There is an advantage to
cropping the frame, which will be explained in detail.
The frames obtained from the camera are at a resolution of 640x480 pixels, which is the default
value. The resolution of the camera can be increased by adjusting its settings, but it is not
possible to decrease it this way. In order to decrease the resolution of the camera, there is
another technique that can be used. This technique is used with another method, and will be
explained there. With this method, the minimum resolution the camera allows is used. There
are some reasons for this, the most important being that if the resolution is increased, there are
more pixels, and thus the computing time increases as well. High computing time is of course
undesirable.
The original height of the frame was 640 pixels, but as previously mentioned, the frame was
cropped. As seen in Figure 3.7a, when there is a curve, the camera also detects points that do
not belong to the track. When the frame is not cropped, the detection of irrelevant points would
result in the undesired production of red Standard Hough Transformation lines. As a result, the upper 100 pixels of the frame height were removed and only the lower 540 pixels were used.
As seen at Figure 3.7b, the red lines are shown only in the last 540 pixels of frame height and
do not cover the irrelevant parts of the frame. If there is a lane, the red lines are very close each
other, but if there is no lane, there is a distance of at least 50 pixels between the red lines. In
Figure 3.7b, there are three different groups of red lines. In each group, there is a lane. Thanks
to the Standard Hough Line Transformation, we know which lanes are between which pixel
columns.
But here there is also another problem. If a curve is to be detected, everything in this step works
as it should (see Figure 3.7b), but if a straight lane is to be detected, a problem occurs. As seen
in Figure 3.8a, the beginning of the middle lane can be grouped with the left lane. In other
words, there are again three different groups for three different lanes but each group of red
lines fails to separate the lanes clearly from each other. As a result, the correct starting points of
the middle and left lanes are not able to be found. In order for the lanes to be detected clearly,
the frame must be divided into two horizontal rows.
As previously mentioned, 100 pixels were already cropped from the top of the image in order
to detect the positions of the lanes clearly and now, the rest of the frame must be divided into
two rows. Based on the experimental results, the top row is 150 pixels high and the bottom
row is 230 pixels high. As a result, the lanes can be grouped into two small frames and in each
small frame, the starting points of lanes must be found. As seen in Figure 3.8b, when the frame
is divided into two pieces, the lanes can be grouped separately.

Step 2 : Secondly, the positions of the lanes should be found. In order to find the positions of the lanes, the Standard Hough Line Transformation is used. But the Standard Hough Line Transformation should not utilize the entire frame; rather, the frame is cropped. There is an advantage to croping the frame, which will be explained in detail.

In this project, the Standard Hough Line Transformation is used different than its actual task. Normally, the Standard Hough Line Transformation detects the straight lines but here it checks, if there are 2 edges in the same vertical of the frame. In other words, if there is a lane, there are 2 edges of the lane in the frame so if there is a lane, there are also Hough Transformation lines. For the Standard Hough Line Transformation is used the function of OpenCV. As previously in Section Standard Hough Transformation explained, for using the this function in OpenCV, some parameters must be setted. One of these parameters was “threshold”, which decides the minimum number of the points to detect a line. In a lane, there are two edges so the Standard Hough lines must be drawn if 2 points in the same vertical are detected. On the other hand, these two points are searched just vertically so another parameter in the Standard Hough Line Transformation function from OpenCV is for the angle, which has to check the points in that angle. Because of the checking just vertically edge with each other, these angle value, which is already named ‘\theta’, is setted ‘CV_PI(180 degree)’.

The frames obtained from the camera are at a resolution of 640x480 pixels, which is the default value. The resolution of the camera can be increased and decreased by adjusting its settings.
The original height of the frame was 640 pixels in this method, but as previously mentioned, the frame was cropped. As seen in Figure 3.7a, the camera detects the edges that do not belong to the track. When the frame is not cropped, the detection of irrelevant edges would result in the undesired production of Standard Hough Transformation lines(which shown in red color). So Hough Transformation is used just for lower 230 pixels. If more than 230 pixels were used for generating the Standard Hough Transformation lines.

As seen in Figure 3.7b, the red lines are shown only in the last 230 pixels of frame height and do not cover the irrelevant parts of the frame.If there is a lane, the red lines are very close each other, but if there is no lane, there is a distance of at least 50 pixels between the red lines. In Figure 3.7b, there are two different groups of red lines. In each group, there is a lane. Thanks to the Standard Hough Line Transformation, it is known, which lanes are between which pixel columns. The right group of Standard Hough Transformation lines signs the right lane and the left group of Standard Hough Transformation lines signs the middle lane.

As recently explained, the positions of the two lanes (right and middle) were detected. Actually, if the more than the lower 230 pixels of the frame would be used, the positions of the all lanes (if the all three lanes can be seen in the frame) but in this case, another problem occurs. As seen in Figure 3.8a, Standard Hough Transformation is implemented for the lower 540 pixels of the frame. As in the same Figure seen, if there is a curve, everything works fine and the positions of the all lanes can be detected. But if there is a straight lane like in Figure 3.8b, the position of the lanes can not be detected correctly. Beginning of the middle lane is grouped with the left lane so it causes the lane detection problems. In other words, there are again three different groups for three different lanes but each group of red lines fails to separate the lanes clearly from each other. As a result, the correct starting points of the middle and left lanes are not able to be found. In order for the lanes to be detected clearly, Standard Hough Line Transformation must be used just for the lower 240 pixels of the frame. End of this step, the positions of the middle and right lane were detected.

Step 3 : After the lanes are grouped separately in two different small frames, the heights of
which are 230 and 150 pixels, the points (pixels) on the lanes must be found in the two small
frames. For that, we have to use Probabilistic Hough Transformation. The Probabilistic Hough
Transformation is a bit different than Standard Hough Line Transformation because Standard
Hough Transformation is more suitable for straight lanes. However, if there is a curve, the
Standard Hough Transformation is not able to detect lanes very well. As previously mentioned,
a line can be represented as y = mx+c or in parametric form, as ρ = x cos θ + y sin θ where
ρ is the perpendicular distance from origin to the line, and θ is the angle formed by this
perpendicular line and horizontal axis measured in counter-clockwise. However, is different
in the case of the Probabilistic Hough Transformation. A line is represented by two or more
points. If the Probabilistic Hough Transformation finds at least two points from the same line,
it represents the two end points of these lines.
In this master’s thesis, the Probabilistic Hough lines are not drawn because just the points (pix-
els) which are detected in the lanes with the Probabilistic Hough Transformation are needed. In Figure 4.9a and Figure 4.9b, the Probabilistic Hough Transformation Points (green pixels) are
shown. The Probabilistic Hough Transformation detected a large number of pixels. By changing
the parameters of the Probabilistic Hough Transformation found in OpenCV, fewer Hough Points
on the lanes are detected, but detecting too few Hough points can also cause some problems
for detecting the lanes. On the other hand, detecting a large number of Hough Points results
in more computing time, which is undesirable. So in this case, the parameters of Probabilistic
Hough Transformation function in OpenCV must be optimized. Thanks to optimization, the best
solution (less computing time and good lane detection) is found.

Step 3 : After the position of the middle and right lane were detected, the Probabilistic Hough Transformation must be implemented. Probabilistic Hough Transformation finds the pixels, which are on the edges of the lanes. The Probabilistic Hough
Transformation is a bit different than Standard Hough Line Transformation because Standard
Hough Transformation is more suitable for straight lanes. However, if there is a curve, the
Standard Hough Transformation is not able to detect lanes very well. As previously in Section Standard Hough Line Transformation mentioned, a line can be represented as y = mx+c or in parametric form, as ρ = x cos θ + y sin θ where ρ is the perpendicular distance from origin to the line, and θ is the angle formed by this perpendicular line and horizontal axis measured in counter-clockwise. However, is different in the case of the Probabilistic Hough Transformation. A line is represented by two or more points. If the Probabilistic Hough Transformation finds at least two points from the same line, it represents the two end points of these lines.

In this project, the function for the Probabilistic Hough Transformation from OpenCV is used, it detects normally lines, but all lanes consist of small lines also even it is a curve. In this project, these small lines on the lanes are detected. These small lines has a starting and end points so instead of the drawning these small lines, the start and end points of these small lines are shown. These all points (pixels) are on the lanes. As previously in Section Probabilistic Hough Transformation explained, there must be setted for Probabilistic Hough Transformation. Here, the value of ‘\ro’, is the resolution in pixels. In this project, this value is setted as 2 and it means, for each 2 pixels, a the lines are searched . Another value in this function is ‘\theta’, which is the resolution in radians. In the Standard Hough Transformation, this value was choosed as 180 degree which can detect just vertical lines but in the Probabilistic Hough Transformation, this value is setted as 1 pixels (CV_PI/180), which can search for each 1 grad angle, the straight lines searched. The ‘threshold’ value decides the minimum number of the points in the same line, to detect a line. This value is used as 2 in this project because it is enough to detect a line, if there are just a start and end points in a line. Another parameter in this function is ‘minLinLength’, which is the minimum length of the line. In this project, Probabilistic Hough Transformation is used to detect small lines in the lanes so this value must be so less. In this project, this value is choosen as 2 because if there are two pixels next to each other in the same lane, these pixels must be detected. The last parameter of the Probabilistic Hough Transformation function is ‘maxLineGap’, which decides to detect small lines if there is more than this value. For the stable lane detection, on the lanes must be detected as soon as more Probabilistic Hough Points so this value is choosed as 2 so this value must be choosen small. These all parameters can be changed and it will effect the computing time.

In Figure 4.9a and Figure 4.9b, the Probabilistic Hough Transformation Points (green pixels) are
shown. The Probabilistic Hough Transformation detected a large number of pixels. By changing
the parameters of the Probabilistic Hough Transformation found in OpenCV, fewer Hough Points
on the lanes are detected, but detecting too few Hough points can also cause some problems
for detecting the lanes. On the other hand, detecting a large number of Hough Points results
in more computing time, which is undesirable. So in this case, the parameters of Probabilistic
Hough Transformation function in OpenCV must be optimized. Thanks to optimization, the best
solution (less computing time and good lane detection) is found.
As previously mentioned, detecting a larger number of Hough Points is increased the computing time. Just because of this reason, the Probabilistic Hough Transformation is not used in the all frame. As seen in Figure 4.9a, in the upper pixels of the frame, there are so many Probabilistic Hough Points which are not relevant the lane so the upper 100 pixels of the frame was cropped, before the Probabilistic Hough Transformation is implemented. In Figure 4.9b, the Probabilistic Hough Points are just on the lanes. With cropping upper 100 pixels, the algorithm is much more faster compare to without cropping the frame.

Step 4 : It is now known in which pixel columns the lanes lie (Step 2), and the points (pixels)
on the lanes are also shown thanks to the Probabilistic Hough Transformation (Step 3), and after
these two steps, the starting points (pixels) of the lanes can be found. In order to do that, the Hough
Points for each group of Hough lines that were found in Step 2 are compared with each other, and
then the last pixels in the columns should be found. If the camera can see three lanes, then the
different starting points for the three different lanes must be found. This means that this process
must be done for all lanes which can be seen in the frame.

Step 4 : It is now known in which pixel columns the middle and right lanes lie (Step 2), and the points (pixels) on the lanes are also shown thanks to Probabilistic Hough Transformation (Step 3), and after these two steps, the starting points (pixels) of the lanes can be found. In order to do that, the Hough Points for each group of Hough lines that were found in Step to compared with each other, and then the lowest pixels in the columns should be found. If the camera can see three lanes, then the different starting points for the three different lanes must be found. This means that this process must be done for all lanes which can be see in the frame. As seen in Step 2, the position of the left lane couldn’t detect although the camera could see the left lane but the left lane was not seen in the lower 230 pixels so the position of the left lane couldn’t detected. In this case, the Hough Points, which are left side of the middle lane position, are compared with each other then the lower pixel is found. It is the starting point (pixel) of the left lane.

Step 5 : The next step in this method is getting the Hough Points which are relevant to the
lanes. Now, for each lane, the Hough Points must be also grouped. For getting the Hough
Points which are relevant to the lanes, what I term the ’rectangle method’ is to be used. In the
rectangle method, a rectangle is drawn for each lane at the starting point found in Step 4, and
the coordinates of all of the Hough Points in that rectangle are saved in a vector. The highest
Hough Point in the rectangle must then be found. From that point, another rectangle must be
drawn, but the sizes of the rectangles are becoming progressively smaller, because the objects
seem smaller the further away they are from the camera. The sizes of the rectangles are also
similar but there is an exception with regard to the middle lane. The middle lane has dashed lines so the rectangles in the middle lane must be bigger than in the left and right lanes. As seen
in Figure 4.10 (rectangles shown in blue), with this method, the noise and the Hough Points
which are not relevant to the lanes are removed.

Step 5 : The next step in this method is getting the Hough Points which are relevant to the
lanes. Now, for each lane, the Hough Points must be also grouped. For getting the Hough
Points which are relevant to the lanes, what I term the ’rectangle method’ is to be used. In the
rectangle method, a rectangle is drawn for each lane at the starting point found in Step 4, and
the coordinates of all of the Hough Points in that rectangle are saved in a vector. The uppest
Hough Points in the rectangle must then be found. From that point, another rectangle must be
drawn, but the sizes of the rectangles are becoming progressively smaller, because the objects
seem smaller the further away they are from the camera. The lower pixels of the frame show the lanes which are close the camera and the upper pixels of the frame show the objects/lanes which are far away from the camera so the size of the size can be adjusted by height of the rectangle. If the rectangle goes to direction of the lower pixels, the size of the size is going to smaller. The sizes of the rectangles are also similar for left and right lanes, but there is an exception with regard to the middle lane. The middle lane has dashed lines so the rectangles in the middle lane must be bigger than in the left and right lanes. As seen in Figure 4.10 (rectangles shown in blue), with this method, the noise and the Hough Points which are not relevant to the lanes are removed. For ‘rectangle method’, a function is defined in the source code. Inputs of this function are, the input image, in which also Probabilistic Hough Transformation was used, starting point of the lane, the vector of the Hough Points and it must be also defined, for which lane this function is used. In which lane, the rectangles are going to drawn must be known, because as previously mentioned, because of the dashed lines in the middle lane, the size of the rectangles are bigger compare to rectangles which are drawn in the left and right lanes.

Step 6 : The next step of this method is curve fitting. Curve Fitting is an algorithm which gives
a mathematical description and this mathematical description provides the best fit for a series
of data points. But in this master’s thesis, the curve fitting to be performed is modified. In this
curve fitting, the coordinates of Hough Points are used but the x and y coordinates of these
Hough Points are swapped, because the y-axes of these coordinates have more range than the
x-axes. As a result, this swap raises the stability of the curve fitting.
After using the Hough Points as input, three different mathematical equations are produced.
One of these equations is for the left lane, another is for the middle lane, and the last equation
is for the right lane. In order to produce these equations, naturally, only the relevant Hough
points are used. For example, for left lane curve equation, only the Hough Points from the left
lane were used.

Step 6 : The next step of this method is curve fitting. Curve Fitting is an algorithm which gives
a mathematical description and this mathematical description provides the best fit for a series
of data points. But in this master’s thesis, the curve fitting to be performed is modified. In this
curve fitting, the coordinates of Hough Points are used but the x and y coordinates of these
Hough Points are swapped, because the y-axes of these coordinates have more range than the
x-axes. As a result, this swap raises the stability of the curve fitting.
After using the Hough Points as input, three different mathematical equations are produced.
One of these equations is for the left lane, another is for the middle lane, and the last equation
is for the right lane. In order to produce these equations, naturally, only the relevant Hough
points are used. For example, for left lane curve equation, only the Hough Points from the left
lane were used. For the curve fitting, a function was implemented in the source code. One of the inputs is the input image. Another input of the function is the vector of the Hough points which are relevant for that lane. In other words, if the curve fitting function will be used for the right lane, then the Hough points must be used, which are relevant to right lane. These points were grouped in Step 5 with Rectangle method. If the fitted curves wanted to be shown in the frame, to differ the fitted curves from each other, a color can be choosen. So color value is also another input in this function. Available colors of fitted curves are red, green and blue. These  variations of the
colors can be increased. The last input value of this function is ‘IPM’. For the tracking the lanes, the fitted curves

For IPM, a function from OpenCV, which is called ’findHomography’, was used. Thanks this function, all Probabilistic Hough Points on the lanes can be converted to the bird’s-eye perspective. It was also possible to convert all pixels from the camera perspective to bird’s-eye perspective, but in that case, it would have been necessary to convert 640x480 pixels, which means 307200 pixels in total. Because of this reason, just the Hough Points, which are relevant to the lanes are converted. There are converted much less pixels compares to convert the all pixels in the frame. IPM algorithm is extrem computationally expensive because of converting just some pixels is made this method efficient. As result, the inputs of the fitted curves are the transformed Hough Points, which were converted from the camera perspective to the bird’s-eye perspective. So output equations of the fitted curves are for the bird’s-eye view.

Step 7 : The next step of this method is plotting the fitted curves produced by the curve fitting
function. We start from first pixel and continue to the 480th pixel vertically and the output values
of the equation for each pixel in the column are found. For each lane, the fitted curves are plotted
in different color. In Figure 4.11, the fitted curve can be seen.

Step 7 : The next step of this method is plotting the fitted curves produced by the curve fitting
function. In this case, the fitted curve starts from the first pixel and continue to the 480th pixel vertically and the output values of the equation for each pixel in the column are found. For each lane, the fitted curves are plotted in different color. For the checking the results, if everything works fine, the input image was also transformed and this fitted curves were plotten in Figure 4.12.